## Slide 1
Clock-Gated 8-bit ALU — Full Architecture
NAND + Tri-State ICG · Opcode-Driven One-Hot Enable · Per-Unit Clock Isolation
Global CLK
Raw clock input
OPCODE [2:0]
3-bit instruction
A [7:0], B [7:0]
Operands
Opcode Decoder
3→8 one-hot en[7:0]
Clock Gate Array
8× NAND + Tri-State
CELL DETAIL
NAND
TRI-ST
×8 cells
Arithmetic Unit
ADD · SUB · MUL · INC · DEC
Logic Unit
AND · OR · XOR
Output MUX
Selects active result
ALU OUT
[7:0] + carry
clk
opcode[2:0]
en[7:0]
A, B
A, B
gclk[0..4]
gclk[5..7]
sel
result
result
alu_out
Clock path
Control / opcode
Data (A, B)
Arithmetic result
Logic result
ALU output
INPUTS
DECODE
CLOCK GATING
FUNCTIONAL
SELECT
OUTPUT

## Slide 2
Clock Gate Cell — NAND + Tri-State
How exactly one unit gets a live clock
clk
en
NAND
TRI-STATE
gclk ✓
Settles during LOW phase
(off critical path)
Only propagation
delay ~0.1ns
Truth Table
clk
en
NAND out
gclk
Effect
0
0
1 (Hi-Z)
0
Idle — no edge possible
0
1
1 (Hi-Z)
0
EN high, clk low — safe
1
0
1 (Hi-Z)
0
★ GATED OFF
1
1
0 (pass)
1
★ ACTIVE — clock passes
en[7:0] — One-Hot Bus
Exactly one bit HIGH per opcode → one ICG cell opens
en[7]
0
XOR
3'b111
en[6]
0
OR
3'b110
en[5]
0
AND
3'b101
en[4]
0
DEC
3'b100
en[3]
0
INC
3'b011
en[2]
0
MUL
3'b010
en[1]
0
SUB
3'b001
en[0]
1
ADD
3'b000
→ gclk ✓ TICKING
Opcode = 000 (ADD) → en = 8'b00000001 → only gclk[0] ticks → 7 units gated OFF

## Slide 3
Power Saving — By The Numbers
100 MHz · 1.8V · Typical ADD-heavy workload (40% ADD, 20% SUB, 15% AND …)
84%
Peak dynamic
power reduction
79%
Structural floor
(any workload)
~0ns
Extra clock delay
(NAND off path)
7/8
Units gated OFF
per cycle
Per-Unit Power Breakdown
Unit
Power
Active %
Avg (gated)
Saved
ADD
3.2 mW
40%
1.28 mW
1.92 mW
SUB
3.0 mW
20%
0.60 mW
2.40 mW
MUL
5.5 mW
8%
0.44 mW
5.06 mW
INC
1.8 mW
2%
0.04 mW
1.76 mW
DEC
1.8 mW
1%
0.02 mW
1.78 mW
AND
2.0 mW
15%
0.30 mW
1.70 mW
OR
2.0 mW
4%
0.08 mW
1.92 mW
XOR
2.2 mW
10%
0.22 mW
1.98 mW
TOTAL
23.0 mW
—
3.67 mW
19.33 mW (84%)
Avg Power: Gated vs Ungated
ADD
3.2
1.28
SUB
3
0.6
MUL
5.5
0.44
AND
2
0.3
XOR
2.2
0.22
Ungated
With clock gating